## Slide 1: Lecture Review
Dr. Yingwu Zhu
10/12/2017

## Slide 2: Our RDT Protocol
Reliable data transfer protocol over unreliable networks
  Checksum, ACK, sequence #, retransmission, timeouts
Limitation: Stop and Wait
  low bandwidth utilization, performance stinks!
Improvement: pipelined protocols

## Slide 3: Pipelined Protocols
Allow multiple outstanding (in-flight) packets
  Sent without acked
Two design choices
  Go-Back-N
  Selective Repeat
jump to case label [-fpermissive]

## Slide 4: Cheat Sheet
 | Go-Back-N | Selective Repeat
Receiver buffer/window | NO | Yes
Out-of-order packets at receivers | Drop them | Buffer them
ACK | Cumulative acks | Individual acks
Timer | One timer associated with the lowest seq # outstanding packet | Multiple timers each associated with a unacked packet
Timeouts | Retransmit all sent yet unacked packets | Retransmit a specific packet
Sender window size | Any size < N* | <= N/2
Pros | Simple | Save unnecessary retransmissions
Cons | Waste bandwidth in networks where out-of-order messages happen a lot | Complexity
*N is the sequence number size