## Slide 1: Congestion Control
Dr. Yingwu Zhu

## Slide 2: Congestion
Best-effort network does not “block” calls
  So, they can easily become overloaded
  Congestion == “Load higher than capacity”
Examples of congestion
  Link layer: Ethernet frame collisions
  Network layer: full IP packet buffers
Excess packets are simply dropped
  And the sender can simply retransmit
queue

## Slide 3: Congestion Collapse
Easily leads to congestion collapse
  Senders retransmit the lost packets
  Leading to even greater load
  … and even more packet loss
Load
Goodput
“congestion
collapse”
Increase in load that results in a decrease in useful work done.
3

## Slide 4: Detect and Respond to Congestion
What does the end host see?
What can the end host change?
?

## Slide 5: Detecting Congestion
Link layer (not covered yet)
  Carrier sense multiple access
  Seeing your own frame collide with others
Network layer
  Observing end-to-end performance
  Packet delay or loss over the path
5

## Slide 6: Responding to Congestion
Upon detecting congestion
  Decrease the sending rate
But, what if conditions change?
  If more bandwidth becomes available,
  … unfortunate to keep sending at a low rate
Upon not detecting congestion: be cautious
  Increase sending rate, a little at a time
  See if packets get through

## Slide 7: TCP Congestion Control
Additive increase, multiplicative decrease
  On packet loss, divide congestion window in half
  On success for last window, increase window linearly
Window
halved
Loss
7
Time

## Slide 8: Why Exponential?
Respond aggressively to bad news
  Congestion is (very) bad for everyone
  Need to react aggressively
Examples:
  Ethernet: double retransmission timer
  TCP: divide sending rate in half
Nice theoretical properties
  Makes efficient use of network resources

## Slide 9: TCP Congestion Control

## Slide 10: Congestion in a Drop-Tail FIFO Queue
Access to the bandwidth: first-in first-out queue
  Packets transmitted in the order they arrive
✗
Access to the buffer space: drop-tail queuing
  If the queue is full, drop the incoming packet

## Slide 11: How it Looks to the End Host
Delay: Packet experiences high delay
Loss: Packet gets dropped along path
How does TCP sender learn this?
  Delay: Round-trip time estimate
  Loss: Timeout and/or duplicate acknowledgments
✗

## Slide 12: TCP Congestion Window
Each TCP sender maintains a congestion window
  Max number of bytes to have in transit (not yet ACK’d)
Adapting the congestion window
  Decrease upon losing a packet: backing off
  Increase upon success: optimistically exploring
  Always struggling to find right transfer rate
Tradeoff
  Pro: avoids needing explicit network feedback
    End-to-end argument
  Con: continually under- and over-shoots “right” rate

## Slide 13: Additive Increase, Multiplicative Decrease
How much to adapt?
  Additive increase: On success of last window of data, increase window by 1 Max Segment Size (MSS)
  Multiplicative decrease: On loss of packet, divide congestion window in half
Much quicker to slow down than speed up!
  Over-sized windows (causing loss) are much worse than under-sized windows (causing lower thruput)
  AIMD: A necessary condition for stability of TCP

## Slide 14: Leads to the TCP “Sawtooth”
Window
halved
Loss
Time

## Slide 15: Receiver Window vs. Congestion Window
Flow control
  Keep a fast sender from overwhelming a slow receiver
Congestion control
  Keep a set of senders from overloading the network
Different concepts, but similar mechanisms
  TCP flow control: receiver window
  TCP congestion control: congestion window
  Sender TCP window =
  min { congestion window, receiver window }

## Slide 16: Sources of poor TCP performance
The below conditions may primarily result in:
Higher pkt latency (B) Greater loss (C) Lower thruput
Larger buffers in routers
Smaller buffers in routers
Smaller buffers on end-hosts
Slow application receivers
Notes: #1: Higher latency (A)
#2: Greater Loss (B)
#3: Lower throughput (C)
#4: Lower throughput (C)

## Slide 17: Starting a New Flow

## Slide 18: How Should a New Flow Start?
Time
Window
halved
Loss
But, could take a long time to get started!
Start slow (a small CWND) to avoid overloading network

## Slide 19: “Slow Start” Phase
Start with a small congestion window
  Initially, CWND is 1 MSS
  So, initial sending rate is 1MSS / RTT
Could be pretty wasteful
  Might be much less than actual bandwidth
  Linear increase takes a long time to accelerate
Slow-start phase (really “fast start”)
  Sender starts at a slow rate (hence the name)
  … but increases rate exponentially until the first loss
  Double CWND every RTT

## Slide 20: Slow Start in Action
Double CWND per round-trip time
D
A
D
D
A
A
D
D
A
A
D
A
Src
Dest
D
A
1
2
4
8

## Slide 21: Slow Start and the TCP Sawtooth
TCP originally had no congestion control
  Source would start by sending entire receiver window
  Led to congestion collapse!
  “Slow start” is, comparatively, slower
Window
halved
Loss
Exponential “slow start”
Time

## Slide 22: Two Kinds of Loss in TCP
Timeout vs. Triple Duplicate ACK
  Which suggests network is in worse shape?
Timeout
  If entire window was lost, buffers may be full
  ...blasting entire CWND would cause another burst
  ...be aggressive: start over with a low CWND
Triple duplicate ACK
  Might be due to bit errors, or “micro” congestion
  ...react less aggressively (halve CWND)
  Then grow linearly (AI)

## Slide 23: Repeating Slow Start After Timeout
t
Window
Slow-start restart: Go back to CWND of 1, but take advantage of knowing the previous value (sz) of CWND: grow exponentially to sz/2, and then AI.
Slow start until reaching half of previous cwnd.
timeout

## Slide 24: Repeating Slow Start After Idle Period
Suppose a TCP connection goes idle for a while
Eventually, the network conditions change
  Maybe many more flows are traversing the link
Dangerous to start transmitting at the old rate
  Previously-idle TCP sender might blast network
  … causing excessive congestion and packet loss
So, some TCP implementations repeat slow start
  Slow-start restart after an idle period

## Slide 25: Fast Recovery
Fast recovery was added with TCP Reno.
Basic idea:: When fast retransmit detects three duplicate ACKs, start the recovery process from congestion avoidance region and use ACKs in the pipe to pace the sending of packets.
Fast Recovery
After Fast Retransmit, half CWND and commence
recovery from this point using linear additive increase
‘primed’ by left over ACKs in pipe.

## Slide 26: Summary: TCP Congestion Control
When CWND is below Threshold, sender in slow-start phase, window grows exponentially.
When CWND is above Threshold, sender is in congestion-avoidance phase, window grows linearly.
When a triple duplicate ACK occurs, Threshold set to CWND/2 and CWND set to Threshold.
When timeout occurs, Threshold set to CWND/2 and CWND is set to 1 MSS.

## Slide 27: Fairness

## Slide 28: TCP Achieves a Notion of Fairness
Effective utilization is not only goal
  We also want to be fair to various flows
Simple definition: equal bandwidth shares
  N flows that each get 1/N of the bandwidth?
But, what if flows traverse different paths?
  Result: bandwidth shared in proportion to RTT

## Slide 29: What About Cheating?
Some folks are more fair than others
  Using multiple TCP connections in parallel (BitTorrent)
  Modifying the TCP implementation in the OS
    Some cloud services start TCP at > 1 MSS
  Use the UDP
What is the impact
  Good guys slow down to make room for you
  You get an unfair share of the bandwidth

## Slide 30: Preventing Cheating
Possible solutions?
  Routers detect cheating and drop excess packets?
  Per user/customer fairness?
  Peer pressure?

## Slide 31: Conclusions
Congestion is inevitable
  Internet does not reserve resources in advance
  TCP actively tries to push the envelope
Congestion can be handled
  Additive increase, multiplicative decrease
  Slow start and slow-start restart
Fundamental tensions
  Feedback from the network?
  Enforcement of “TCP friendly” behavior?