## Slide 1: Lecture Review
Dr. Yingwu Zhu
10/26/2017

## Slide 2: Network Layer: IP Network
Best-effort global packet delivery
  Host-to-host: source IP to destination IP
  Narrow waist
  Performance and robustness are important
Upper-layer protocols can provide richer functionality
  reliability,…
Connect with various networking technologies
  Wired, wireless, …

## Slide 3: Network Routers
Control plane
  Softwares
  Routing: run some routing protocol(s) to populate forwarding (routing) table
Data plane
  Adapters (NICs) & ports, memory, switching fabric
  Forwarding: based on its dest IP address, forward a packet to an output port, via the switch fabric, hopefully at the link speed
  Buffering: when outgoing link demand > link speed
    Queueing delay and packet drops

## Slide 4: IP Addresses
4 bytes
Hierarchical addressing is important to scalability
  12.34.158.0/24 is a 24-bit prefix with 28 addresses
  Network ID + Host ID
IP addresses are allocated by contiguous blocks (prefixes)
Scalability
  Smaller forwarding table size (prefix-based entries)
  Fast to update routing states
  Routing state is not affected due to nodes addition/removal within a network
  ~400,000 prefixes

## Slide 5: Longest Prefix Match
Routers make forwarding decisions
  Longest prefix match of a destination IP address with the forwarding table
Not exact match!
4.0.0.0/8
4.83.128.0/17
201.10.0.0/21
201.10.6.0/23
126.255.103.0/24
201.10.6.17
destination
forwarding table
Serial0/0.1
outgoing link