## Slide 1: Link Layer
Dr. Yingwu Zhu

## Slide 2: Protocol Layers
HTTP
TCP
IP
Ethernet
interface
HTTP
TCP
IP
Ethernet
interface
IP
IP
Ethernet
interface
Ethernet
interface
SONET
interface
SONET
interface
host
host
router
router
HTTP message
TCP segment
IP packet
IP packet
IP packet
Ethernet frame
Ethernet frame
SONET frame

## Slide 3: Link = Medium + Adapters

## Slide 4: What is a Link?
Communication Medium
Network Adapter

## Slide 5: Broadcast Links: Shared Media

## Slide 6: Adaptors Communicating
Sending side
  Encapsulates packet in a frame
  Adds error checking bits, flow control, etc.
Receiving side
  Looks for errors, flow control, etc.
  Extracts datagram and passes to receiving node
sending
node
frame
receiving
node
packet
frame
adapter
adapter
link layer protocol
packet

## Slide 7: Link-Layer Services
Encoding
  Represent the 0s and 1s
Framing
  Encapsulate packet into frame, adding header/trailer
Error detection
  Receiver detecting errors with checksums
Error correction
  Receiver optionally correcting errors
Flow control
  Pacing between sending and receiving nodes

## Slide 8: Link-Layer Services (Cont.)
Reliable delivery between adjacent nodes
  We know how to do it.
  Seldom used in low bit-error links (fiber)
Half-duplex and full-duplex
  With half duplex, nodes at both ends of link can transmit, but not at same time

## Slide 9: Addresses

## Slide 10: Medium Access Control Address
Identify the sending and receiving adapter
  Unique identifier for each network adapter
  Identifies the intended receiver(s) of the frame
  … and the sender who sent the frame

## Slide 11: Medium Access Control Address
MAC address (e.g., 00-15-C5-49-04-A9)
  Numerical address used within a link
  Unique, hard-coded in the adapter when it is built
  Flat name space of 48 bits
Hierarchical allocation: Global uniqueness!
  Blocks: assigned to vendors (e.g., Dell) by the IEEE
  Adapters: assigned by the vendor from its block
Broadcast address (i.e., FF-FF-FF-FF-FF-FF)
  Send the frame to all adapters

## Slide 12: As an Aside: Promiscuous Mode
Normal adapter: receives frames sent to
  The local MAC address
  Broadcast address FF-FF-FF-FF-FF-FF
Promiscuous mode
  Receive everything, independent of destination MAC
Useful for packet sniffing
  Network monitoring
  E.g., wireshark, tcpdump

## Slide 13: Why Not Just Use IP Addresses?
Links can support any network protocol
  Not just for IP (e.g., IPX, Appletalk, X.25, …)
  Different addresses on different kinds of links
An adapter may move to a new location
  So, cannot simply assign a static IP address
  Instead, must reconfigure the adapter’s IP address
Must identify the adapter during bootstrap
  Need to talk to the adapter to assign it an IP address

## Slide 14: Who Am I: Acquiring an IP Address
????
DHCP server
Dynamic Host Configuration Protocol (DHCP)
  Broadcast “I need an IP address, please!”
  Response “You can have IP address 1.2.3.4.”
71-65-F7-2B-08-53
1A-2F-BB-76-09-AD
0C-C4-11-6F-E3-98
1.2.3.6

## Slide 15: Who Are You: Discovering the Receiver
Address Resolution Protocol (ARP)
  Broadcast “who has IP address 1.2.3.6?”
  Response “0C-C4-11-6F-E3-98 has 1.2.3.6!”
71-65-F7-2B-08-53
1.2.3.4
1.2.3.5
0C-C4-11-6F-E3-98
1.2.3.6

## Slide 16: Sharing the Medium

## Slide 17: Collisions
Single shared broadcast channel
  Avoid having multiple nodes speaking at once
  Otherwise, collisions lead to garbled data
71-65-F7-2B-08-53
1A-2F-BB-76-09-AD
0C-C4-11-6F-E3-98

## Slide 18: Multi-Access Protocol
Divide the channel into pieces
  In time
  In frequency
Take turns
  Pass a token for the right to transmit
Punt
  Let collisions happen
  … and detect and recover from them
18

## Slide 19: Like Human Conversation…
Carrier sense
  Listen before speaking
  …and don’t interrupt!
Collision detection
  Detect simultaneous talking
  … and shut up!
Random access
Listen to collision
(min packet size 2tb) t-propagation delay
  Wait for a random period of time
  … before trying to talk again!
19

## Slide 20: Carrier Sense Multiple Access
Listen for other senders
  Then transmit your data
Collisions can still occur
  Propagation delay
  Wasted transmission

## Slide 21: CSMA/CD Collision Detection
Detect collision
  Abort transmission
  Jam the link
Wait random time
  Transmit again
Hard in wireless
  Must receive data while transmitting
    One antenna for send/recv, powerful sending signals

## Slide 22: Ethernet

## Slide 23: Ethernet
Dominant wired LAN technology
First widely used LAN technology
Kept up with speed race: 10 Mbps – 40 Gbps
Metcalfe’s
Ethernet
sketch
23

## Slide 24: Ethernet Uses CSMA/CD
Carrier Sense: wait for link to be idle
  Channel idle: start transmitting
  Channel busy: wait until idle
Collision Detection: listen while transmitting
  No collision: transmission is complete
  Collision: abort transmission, and send jam signal
Random Access: exponential back-off
  After collision, wait random time before trying again
  After mth collision, choose K randomly from {0, …, 2m-1}
  … and wait for K*512 bit times before trying again
24

## Slide 25: Limitations on Ethernet Length
Latency depends on physical length of link
  Time to propagate a packet from one end to other
Suppose A sends a packet at time t
  And B sees an idle line at a time just before t+d
  … so B happily starts transmitting a packet
B detects a collision, and sends jamming signal
  But A doesn’t see collision till t+2d
latency d
A
B
25

## Slide 26: Limitations on Ethernet Length
A needs to wait for time 2d to detect collision
  So, A should keep transmitting during this period
  … and keep an eye out for a possible collision
Imposes restrictions on Ethernet
  Maximum length of the wire: 2500 meters
  Minimum length of the packet: 512 bits (64 bytes)
latency d
A
B
26

## Slide 27: Ethernet Frame Structure
Sending adapter encapsulates packet in frame
Preamble: synchronization
  Seven bytes with pattern 10101010, followed by one byte with pattern 10101011
  Used to synchronize receiver, sender clock rates
27

## Slide 28: Ethernet Frame Structure
Addresses: source and destination MAC addresses
  Adaptor passes frame to network-level protocol
    If destination is local MAC address or broadcast address
  Otherwise, adapter discards frame
Type: indicates the higher layer protocol
  Usually IP
  But also Novell IPX, AppleTalk, …
CRC: cyclic redundancy check
  Checked at receiver
  If error is detected, the frame is simply dropped
28

## Slide 29: Unreliable, Connectionless Service
Connectionless
  No handshaking between send and receive adapter
Unreliable
  Receiving adapter doesn’t send ACKs or NACKs
  Packets passed to network layer can have gaps
  Gaps can be filled by transport protocol (e.g., TCP)
  Otherwise, the application will see the gaps
29

## Slide 30: Hubs and Switches

## Slide 31: Physical Layer: Repeaters
Distance limitation in local-area networks
  Electrical signal becomes weaker as it travels
  Imposes a limit on the length of a LAN
Repeaters join LANs together
  Analog electronic device
  Continuously monitors electrical signals
  Transmits an amplified copy
31

## Slide 32: Physical Layer: Hubs
Joins multiple input lines electrically
  Designed to hold multiple line cards
  Do not necessarily amplify the signal
Very similar to repeaters
  Also operates at the physical layer
hub
hub
hub
hub
32

## Slide 33: Limitations of Repeaters and Hubs
One large shared link
  Each bit is sent everywhere
  So, aggregate throughput is limited
Cannot support multiple LAN technologies
  Does not buffer or interpret frames
  Can’t interconnect between different rates/formats
Limitations on maximum nodes and distances
  Shared medium imposes length limits
  E.g., cannot go beyond 2500 meters on Ethernet
33

## Slide 34: Link Layer: Bridges
Connects two or more LANs at the link layer
  Extracts destination address from the frame
  Looks up the destination in a table
  Forwards the frame to the appropriate segment
Each segment can carry its own traffic
host
host
host
host
host
host
host
host
host
host
host
host
Bridge
34

## Slide 35: Link Layer: Switches
Typically connects individual computers
  A switch is essentially the same as a bridge
  … though typically used to connect hosts
Supports concurrent communication
  Host A can talk to C, while B talks to D
switch
A
B
C
D
35

## Slide 36: Bridges/Switches: Traffic Isolation
Switch filters packets
  Frame only forwarded to the necessary segments
  Segments can support separate transmissions
hub
hub
hub
switch/bridge
segment
segment
segment
36

## Slide 37: Switches vs. Hubs
Compared to hubs, Ethernet switches support
  Larger geographic span
  Similar span
  Smaller span
Compared to hubs, switches provides
  (a) Higher load on links
  (b) Less privacy
  (c) Heterogenous communication technologies

## Slide 38: Switches vs. Hubs
Compared to hubs, Ethernet switches support
  Larger geographic span
  Similar span
  Smaller span
Compared to hubs, switches provides
  (a) Higher load on links
  (b) Less privacy
  (c) Heterogenous communication technologies

## Slide 39: Self Learning: Building the Table
When a frame arrives
  Inspect the source MAC address
  Associate the address with the incoming interface
  Store the mapping in the switch table
  Use a timer to eventually forget the mapping
A
B
C
D
Switch learns how to reach A.
39

## Slide 40: Self Learning: Handling Misses
When frame arrives with unfamiliar destination
  Forward the frame out all of the interfaces
  … except for the one where the frame arrived
  Hopefully, this case won’t happen very often!
A
B
C
D
When in doubt, shout!
40

## Slide 41: Summary: Multiple Layers
Different devices switch different things
  Network layer: packets (routers)
  Link layer: frames (bridges and switches)
  Physical layer: electrical signals (repeaters and hubs)
Application
Transport
Router
Bridge, switch
Repeater, hub
Frame header
Packet header
TCP header
User
data
41

## Slide 42: Conclusion
Links
  Connect two or more network adapters
  … each with a unique address
  … over a shared communication medium