## Slide 1: Network Layer
Dr. Yingwu Zhu

## Slide 2: IP Protocol Stack: Key Abstractions
Best-effort local packet delivery
Best-effort global packet delivery
Reliable streams
Applications
Messages
Link
Network
Transport
Application

## Slide 3: Best-Effort Global Packet Delivery
Host-to-Host delivery
Analogy: Airport-to-Airport delivery

## Slide 4: Circuit Switching (e.g., Phone Network)
Source establishes connection
  Reserve resources along hops in the path
Source sends data
  Transmit data over the established connection
Source tears down connection
  Free the resources for future connections

## Slide 5: Circuit Switching: Static Allocation
Q: Frequency-Division vs. Time-Division
time
time

## Slide 6: Circuit Switching: Static Allocation
Time-division
  Each circuit allocated certain time slots
Frequency-division
  Each circuit allocated certain frequencies
time
frequency
time

## Slide 7: Packet Switching
Message divided into packets
  Header identifies the destination address
Packets travel separately through the network
  Forwarding based on the destination address
  Packets may be buffered temporarily
Destination reconstructs the message

## Slide 8: Packet Switching: Statistical (Time Division) Multiplexing
Packets
Intuition: Traffic by computer end-points is bursty!
  Versus: Telephone traffic not bursty (e.g., constant 56 kbps)
  One can use network while others idle
Packet queuing in network: tradeoff space for time
  Handle short periods when outgoing link demand > link speed
Notes: STDM can be with cirtcuits (packets tagged with ID and preestablished state in switches) or with full packet switching (need full addressing in each packet)

## Slide 9: Best Effort: Celebrating Simplicity
Packets may be lost, corrupted, reordered
Never having to say you’re sorry…
  Don’t reserve bandwidth and memory
  Don’t do error detection and correction
  Don’t remember from one packet to next
Easier to survive failures
  Transient disruptions are okay during failover
Easier to support on many kinds of links
  Important for interconnecting different networks
9

## Slide 10: Is Best Effort Good Enough?
Packet loss and delay
  Sender can resend
Packet corruption
  Receiver can detect, and sender can resend
Out-of-order delivery
  Receiver can put the data back in order
Packets follow different paths
  Doesn’t matter
Network failure
  Drop the packet
Network congestion
  Drop the packet

## Slide 11: Packet vs. Circuit Switching?
Predictable performance
Network never blocks senders
Reliable, in-order delivery
Low delay to send data
Simple forwarding
No overhead for packet headers
High utilization under most workloads
No per-connection network state
Circuit
Packet
Circuit
Packet
Circuit
Circuit
Packet
Packet

## Slide 12: Network Addresses

## Slide 13: IP Address (IPv4)
A unique 32-bit number
Identifies an interface (on a host, on a router, …)
Represented in dotted-quad notation
00001100
00100010
10011110
00000101
12
34
158
5

## Slide 14: Grouping Related Hosts
The Internet is an “inter-network”
  Used to connect networks together, not hosts
  Need to address a network (i.e., group of hosts)
LAN = Local Area Network
WAN = Wide Area Network
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN

## Slide 15: Scalability Challenge
Suppose hosts had arbitrary addresses
  Then every router would need a lot of information
  …to know how to direct packets toward every host
host
host
host
LAN 1
...
host
host
host
LAN 2
...
router
router
router
WAN
WAN
1.2.3.4
5.6.7.8
2.4.6.8
1.2.3.5
5.6.7.9
2.4.6.9
1.2.3.4
1.2.3.5
forwarding table

## Slide 16: Hierarchical Addressing in U.S. Mail
Addressing in the U.S. mail
  Zip code: 08540
  Building: 35 Olden Street
  Room in building: 308
  Name of occupant: Mike Freedman
Forwarding the U.S. mail
  Deliver to the post office in the zip code
  Assign to mailman covering the building
  Drop letter into mailbox for building/room
  Give letter to the appropriate person
???
16

## Slide 17: Hierarchical Addressing: IP Prefixes
Network and host portions (left and right)
12.34.158.0/24 is a 24-bit prefix with 28 addresses
00001100
00100010
10011110
00000101
Network (24 bits)
Host (8 bits)
12
34
158
5

## Slide 18: IP Address and 24-bit Subnet Mask
00001100
00100010
10011110
00000101
12
34
158
5
11111111
11111111
11111111
00000000
255
255
255
0
Address
Mask

## Slide 19: Scalability Improved
Number related hosts from a common subnet
  1.2.3.0/24 on the left LAN
  5.6.7.0/24 on the right LAN
host
host
host
LAN 1
...
host
host
host
...
router
router
router
WAN
WAN
1.2.3.4
1.2.3.7
1.2.3.156
5.6.7.8
5.6.7.9
5.6.7.212
1.2.3.0/24
5.6.7.0/24
forwarding table
LAN 2

## Slide 20: Easy to Add New Hosts
No need to update the routers
  E.g., adding a new host 5.6.7.213 on the right
  Doesn’t require adding a new forwarding-table entry
host
host
host
LAN 1
...
host
host
LAN 2
...
router
router
router
WAN
WAN
1.2.3.4
1.2.3.7
1.2.3.156
5.6.7.8
5.6.7.9
5.6.7.212
host
5.6.7.213
1.2.3.0/24
5.6.7.0/24
forwarding table
host

## Slide 21: History of IP Address Allocation

## Slide 22: Classful Addressing
In the olden days, only fixed allocation sizes
  Class A: 0*
    Very large /8 blocks (e.g., MIT has 18.0.0.0/8)
  Class B: 10*
    Large /16 blocks (e.g,. Princeton has 128.112.0.0/16)
  Class C: 110*
    Small /24 blocks (e.g., AT&T Labs has 192.20.225.0/24)
  Class D: 1110* for multicast groups
  Class E: 11110* reserved for future use
This is why folks use dotted-quad notation!

## Slide 23: Classless Inter-Domain Routing (CIDR)
IP Address : 12.4.0.0 IP Mask: 255.254.0.0
00001100
00000100
00000000
00000000
11111111
11111110
00000000
00000000
Address
Mask
for hosts
Network Prefix
Written as 12.4.0.0/15
Use two 32-bit numbers to represent network:
  Network number = IP address + Mask

## Slide 24: Hierarchical Address Allocation
Hierarchy is key to scalability
  Address allocated in contiguous chunks (prefixes)
  Today, the Internet has about 400,000 prefixes
12.0.0.0/8
12.0.0.0/16
12.254.0.0/16
12.1.0.0/16
12.2.0.0/16
12.3.0.0/16
:
:
:
12.3.0.0/24
12.3.1.0/24
:
:
12.3.254.0/24
12.253.0.0/19
12.253.32.0/19
12.253.160.0/19
:
:
:
:
:

## Slide 25: Obtaining a Block of Addresses
Internet Corporation for Assigned Names and Numbers (ICANN)
  Allocates large blocks to Regional Internet Registries
Regional Internet Registries (RIRs)
  E.g., ARIN (American Registry for Internet Numbers)
  Allocates to ISPs and large institutions
Internet Service Providers (ISPs)
  Allocate address blocks to their customers
  Who may, in turn, allocate to their customers…
25

## Slide 26: Pre-CIDR (1988-1994): Steep Growth
Growth faster than improvements in equipment capability

## Slide 27: CIDR (1994-1996): Much Flatter
Efforts to aggregate

## Slide 28: CIDR Growth (1996-1998): Roughly Linear
Good use of aggregation, and peer pressure!

## Slide 29: DotCom Boom (1998-2001): Steep Growth
Internet boom and increased multi-homing

## Slide 30: Long Term Growth (1989-2005)
Today we are up to ~400,000 prefixes
Pre CIDR
CIDR’s
effect
DotCom
Boom
Post Boom

## Slide 31: Packet Forwarding

## Slide 32: Hop-by-Hop Packet Forwarding
Each router has a forwarding table
  Maps destination address to outgoing interface
Upon receiving a packet
  Inspect the destination address in the header
  Index into the table
  Determine the outgoing interface
  Forward the packet out that interface
Then, the next router in the path repeats

## Slide 33: IP Router
Switching
Fabric
Processor
Adapter
Adapter
Adapter
Adapter
Adapter
Adapter
data plane
control plane

## Slide 34: Switch Fabric: From Input to Output
Lookup
Address
Update
Header
Header Processing
Address
Table
Lookup
Address
Update
Header
Header Processing
Address
Table
Lookup
Address
Update
Header
Header Processing
Address
Table
Queue
Packet
Buffer
Memory
Queue
Packet
Buffer
Memory
Queue
Packet
Buffer
Memory
Data
Hdr
Data
Hdr
Data
Hdr
1
2
N
1
2
N

## Slide 35: Separate Forwarding Entry Per Prefix
Prefix-based forwarding
  Map the destination address to matching prefix
  Forward to the outgoing interface
host
host
host
LAN 1
...
host
host
host
LAN
...
router
router
router
WAN
WAN
1.2.3.4
1.2.3.7
1.2.3.156
5.6.7.8
5.6.7.9
5.6.7.212
1.2.3.0/24
5.6.7.0/24
forwarding table

## Slide 36: CIDR Makes Packet Forwarding Harder
Forwarding table may have many matches
  E.g., entries for 201.10.0.0/21 and 201.10.6.0/23
  The IP address 201.10.6.17 would match both!
201.10.0.0/21
201.10.0.0/22
201.10.4.0/24
201.10.5.0/24
201.10.6.0/23
Provider 1
Provider 2
201.10.6.0/23

## Slide 37: Longest Prefix Match Forwarding
Destination-based forwarding
  Packet has a destination address
  Router identifies longest-matching prefix
Cute algorithmic problem: very fast lookups
4.0.0.0/8
4.83.128.0/17
201.10.0.0/21
201.10.6.0/23
126.255.103.0/24
201.10.6.17
destination
forwarding table
Serial0/0.1
outgoing link

## Slide 38: Creating a Forwarding Table
Entries can be statically configured
  E.g., “map 12.34.158.0/24 to Serial0/0.1”
But, this doesn’t adapt
  To failures
  To new equipment
  To the need to balance load
That is where the control plane comes in
  Routing protocols

## Slide 39: Data, Control, & Management Planes
 | Data | Control | Management
Time-scale | Packet (ns) | Event (10 ms to sec) | Human (min to hours)
Tasks | Forwarding, buffering, filtering, scheduling | Routing, signaling | Analysis, configuration
Location | Line-card hardware | Router software | Humans or scripts
39
Switching
Fabric
Processor

## Slide 40: Q’s: MAC vs. IP Addressing
Hierarchically allocated
    A) MAC B) IP C) Both D) Neither
Organized topologically
  A) MAC B) IP C) Both D) Neither
Forwarding via exact match on address
A) MAC B) IP C) Both D) Neither
Automatically calculate forwarding by observing data
A) Ethernet switches B) IP routers C) Both D) Neither
Per connection state in the network
A) MAC B) IP C) Both D) Neither
Per host state in the network
A) MAC B) IP C) Both D) Neither

## Slide 41: Q’s: MAC vs. IP Addressing
Hierarchically allocated
    A) MAC B) IP C) Both D) Neither
Organized topologically
  A) MAC B) IP C) Both D) Neither
Forwarding via exact match on address
A) MAC B) IP C) Both D) Neither
Automatically calculate forwarding by observing data
A) Ethernet switches B) IP routers C) Both D) Neither
Per connection state in the network
A) MAC B) IP C) Both D) Neither
Per host state in the network
A) MAC B) IP C) Both D) Neither

## Slide 42: IP Packet Format

## Slide 43: IP Packet Structure
4-bit
Version
4-bit
Header
Length
8-bit
Type of Service
(TOS)
16-bit Total Length (Bytes)
16-bit Identification
3-bit
Flags
13-bit Fragment Offset
8-bit Time to
Live (TTL)
8-bit Protocol
16-bit Header Checksum
32-bit Source IP Address
32-bit Destination IP Address
Options (if any)
Payload

## Slide 44: IP Fragmentation & Reassembly
Problem: A router may receive a packet larger than the maximum transmission unit (MTU) of the outgoing link.
  different link types, different MTUs
Solution: large IP datagram divided (“fragmented”) within net
  one datagram becomes several datagrams
  “reassembled” only at final destination, why?
  IP header bits used to identify, order related fragments
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly
E.g., bytes. Ethernet frames carry up to 1500 bytes, frames for some wide-area links carry no more than 576 (MTU: the max of data a link-layer frame can carry)

## Slide 45: IP Fragmentation and Reassembly
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
One large datagram becomes
several smaller datagrams
Example
4000 byte datagram
MTU = 1500 bytes
1480 bytes in data field
offset =
1480/8
Note: the offset value is specified in units of 8-byte chunks!!!

## Slide 46: Fragmentation
Fragments are re-assembled by the destination host; not by intermediate routers.
To avoid fragmentation, hosts commonly use path MTU discovery to find the smallest MTU along the path.
Path MTU discovery involves sending various size datagrams until they do not require fragmentation along the path.
Most links use MTU>=1500bytes today.
Try: traceroute www.berkeley.edu 500 –F and traceroute www.berkeley.edu 1501 -F
-F: Set the "don't fragment" bit, return error it is too long

## Slide 47: Conclusion
Best-effort global packet delivery
  Simple end-to-end abstraction
  Enables higher-level abstractions on top
  Doesn’t rely on much from the links below
IP addressing and forwarding
  Hierarchy for scalability and decentralized control
  Allocation of IP prefixes
  Longest prefix match forwarding

## Slide 48: Backup Slides

## Slide 49: IP Header: Version, Length, ToS
Version number (4 bits)
  Necessary to know what other fields to expect
  Typically “4” (for IPv4), and sometimes “6” (for IPv6)
Header length (4 bits)
  Number of 32-bit words in the header
  Typically “5” (for a 20-byte IPv4 header)
  Can be more when “IP options” are used
Type-of-Service (8 bits)
  Allow different packets to be treated differently
  Low delay for audio, high bandwidth for bulk transfer

## Slide 50: IP Header: Length, Fragments, TTL
Total length (16 bits)
  Number of bytes in the packet
  Max size is 63,535 bytes (216 -1)
  … though most links impose smaller limits
Fragmentation information (32 bits)
  Supports dividing a large IP packet into fragments
  … in case a link cannot handle a large IP packet
Time-To-Live (8 bits)
  Used to identify packets stuck in forwarding loops
  … and eventually discard them from the network

## Slide 51: IP Header: Transport Protocol
Protocol (8 bits)
  Identifies the higher-level protocol
    E.g., “6” for the Transmission Control Protocol (TCP)
    E.g., “17” for the User Datagram Protocol (UDP)
  Important for demultiplexing at receiving host
    Indicates what kind of header to expect next
IP header
IP header
TCP header
UDP header
protocol=6
protocol=17

## Slide 52: IP Header: Header Checksum
Checksum (16 bits)
  Sum of all 16-bit words in the header
  If header bits are corrupted, checksum won’t match
  Receiving discards corrupted packets
134
+ 212
= 346
134
+ 216
= 350
Mismatch!

## Slide 53: IP Header: To and From Addresses
Destination IP address (32 bits)
  Unique identifier for the receiving host
  Allows each node to make forwarding decisions
Source IP address (32 bits)
  Unique identifier for the sending host
  Recipient can decide whether to accept packet
  Enables recipient to send a reply back to source