## Slide 1: Routing Convergence
Dr. Yingwu Zhu
peer
peer
advertisements
traffic

## Slide 2: Routing Changes
Topology changes: new route to the same place
Host mobility: route to a different place

## Slide 3: Topology Changes

## Slide 4: Two Types of Topology Changes
Planned
  Maintenance: shut down a node or link
  Energy savings: shut down a node or link
  Traffic engineering: change routing configuration
Unplanned Failures
  Fiber cut, faulty equipment, power outage, software bugs, …

## Slide 5: Detecting Topology Changes
Beaconing
  Periodic “hello” messages in both directions
  Detect a failure after a few missed “hellos”
Performance trade-offs
  Detection delay
  Overhead on link bandwidth and CPU
  Likelihood of false detection
“hello”

## Slide 6: Routing Convergence: Link-State Routing

## Slide 7: Convergence
Control plane
  All nodes have consistent information
Data plane
  All nodes forward packets in a consistent way
3
2
2
1
1
4
1
4
5
3

## Slide 8: Transient Disruptions
Detection delay
  A node does not detect a failed link immediately
  … and forwards data packets into a “blackhole”
  Depends on timeout for detecting lost hellos
3
2
2
1
1
4
1
4
5
3

## Slide 9: Transient Disruptions
Inconsistent link-state database
  Some routers know about failure before others
  Inconsistent paths cause transient forwarding loops
3
2
2
1
1
4
1
4
3
3
2
2
1
1
4
1
4
5
3

## Slide 10: Convergence Delay
Sources of convergence delay
  Detection latency
  Updating control-plane information
  Computing and install new forwarding tables
Performance during convergence period
  Lost packets due to blackholes and TTL expiry
  Looping packets consuming resources
  Out-of-order packets reaching the destination
Very bad for VoIP, online gaming, and video

## Slide 11: Reducing Convergence Delay
Faster detection
  Smaller hello timers, better link-layer technologies
Faster control plane
  Flooding immediately
  Sending routing messages with high-priority
Faster computation
  Faster processors, and incremental computation
Faster forwarding-table update
  Data structures supporting incremental updates

## Slide 12: Slow Convergence in Distance-Vector Routing

## Slide 13: Distance Vector: Link Cost Changes
Link cost decreases and recovery
  Node updates the distance table
  If cost change in least cost path, notify neighbors
X
Z
1
4
50
Y
1
DY = Distances known to Y

## Slide 14: Distance Vector: Link Cost Changes
Link cost decreases and recovery
  Node updates the distance table
  If cost change in least cost path, notify neighbors
X
Z
1
4
50
Y
1
DY = Distances known to Y

## Slide 15: Distance Vector: Link Cost Changes
Link cost decreases and recovery
  Node updates the distance table
  If cost change in least cost path, notify neighbors
X
Z
1
4
50
Y
1
“good
news
travels
fast”
DY = Distances known to Y

## Slide 16: Distance Vector: Link Cost Changes
Link cost increases and failures
  Bad news travels slowly
  “Count to infinity” problem!
X
Z
1
4
50
Y
60

## Slide 17: Distance Vector: Link Cost Changes
Link cost increases and failures
  Bad news travels slowly
  “Count to infinity” problem!
X
Z
1
4
50
Y
60
algorithm
continues
on!

## Slide 18: Distance Vector: Poison Reverse
If Z routes through Y to get to X :
  Z tells Y its (Z’s) distance to X is infinite (so Y won’t route to X via Z)
  Still, can have problems in larger networks
X
Z
1
4
50
Y
60
algorithm
terminates

## Slide 19: Redefining Infinity
Avoid “counting to infinity”
  By making “infinity” smaller!
Routing Information Protocol (RIP)
  All links have cost 1
  Valid path distances of 1 through 15
  … with 16 representing infinity
Used mainly in small networks

## Slide 20: Reducing Convergence Time With Path-Vector Routing (e.g., Border Gateway Protocol)

## Slide 21: Path-Vector Routing
Extension of distance-vector routing
  Support flexible routing policies
  Avoid count-to-infinity problem
Key idea: advertise the entire path
  Distance vector: send distance metric per dest d
  Path vector: send the entire path for each dest d
3
2
1
d
“d: path (2,1)”
“d: path (1)”
data traffic
data traffic

## Slide 22: Faster Loop Detection
Node can easily detect a loop
  Look for its own node identifier in the path
  E.g., node 1 sees itself in the path “3, 2, 1”
Node can simply discard paths with loops
  E.g., node 1 simply discards the advertisement
“d: path (3,2,1)”
3
2
1
“d: path (2,1)”
“d: path (1)”

## Slide 23: BGP Session Failure
BGP runs over TCP
  BGP only sends updates when changes occur
  TCP doesn’t detect lost connectivity on its own
Detecting a failure
  Keep-alive: 60 seconds
  Hold timer: 180 seconds
Reacting to a failure
  Discard all routes learned from neighbor
  Send new updates for any routes that change
AS1
AS2

## Slide 24: Routing Change: Before and After
0
1
2
3
(1,0)
(2,0)
(3,1,0)
0
1
2
3
(2,0)
(1,2,0)
(3,2,0)
24

## Slide 25: Routing Change: Path Exploration
AS 1
  Delete the route (1,0)
  Switch to next route (1,2,0)
  Send route (1,2,0) to AS 3
AS 3
  Sees (1,2,0) replace (1,0)
  Compares to route (2,0)
  Switches to using AS 2
0
1
2
3
(2,0)
(1,2,0)
(3,2,0)

## Slide 26: Routing Change: Path Exploration
Initial: All AS use direct
Then destination 0 dies
  All ASes lose direct path
  All switch to longer paths
  Eventually withdrawn
How many intermediate routes following (2,0) withdrawal until no route known to 2?
  (2,0)  (2,1,0)  (2,3,0)  (2,1,3,0)  null
1
2
3
0
(1,0)
(1,2,0)
(1,3,0)
(2,0)
(2,1,0)
(2,3,0)
(2,1,3,0)
(3,0)
(3,1,0)
(3,2,0)

## Slide 27: BGP Converges Slowly
Path vector avoids count-to-infinity
  But, ASes still must explore many alternate paths to find highest-ranked available path
Fortunately, in practice
  Most popular destinations have stable BGP routes
  Most instability lies in a few unpopular destinations
Still, lower BGP convergence delay is a goal
  Can be tens of seconds to tens of minutes
27

## Slide 28: BGP Instability
28

## Slide 29: Stable Paths Problem
Does every node have a stable route to one destination node?

## Slide 30: Stable Paths Problem (SPP) Instance
1
Node
  BGP-speaking router
  Node 0 is destination
Edge
  BGP adjacency
Permitted paths
  Set of routes to 0 at each node (this set always contains “null path”, which is always the least preferred, not shown here)
  Ranking of the paths
2
5
5 2 1 0
0
2 1 0
2 0
1 3 0
1 0
3 0
4 2 0
4 3 0
3
4
2
1
most preferred
…
least preferred
30

## Slide 31: A Solution to a Stable Paths Problem
1
A solution is an assignment of permitted paths to each node such that
node u’s assigned path is either the null path or is a path uwP, where wP is assigned to node w and {u,w} is an edge in the graph
each node is assigned the highest ranked path among those consistent with the paths assigned to its neighbors.
2
5
5 2 1 0
0
2 1 0
2 0
1 3 0
1 0
3 0
4 2 0
4 3 0
3
4
2
1
most preferred
…
least preferred
31

## Slide 32: Example: SHORTEST1
1
2
4
3
0
2 0
2 1 0
1 0
1 3 0
4 3 0
4 2 0
3 0

## Slide 33: Example: SHORTEST1 (Solution)
1
2
4
3
0
2 0
2 1 0
1 0
1 3 0
4 3 0
4 2 0
3 0

## Slide 34: Example: SHORTEST2
1
2
4
3
0
2 0
2 1 0
1 0
1 3 0
4 2 0
4 3 0
3 0

## Slide 35: Example: SHORTEST2 (Solution)
1
2
4
3
0
2 0
2 1 0
1 0
1 3 0
4 2 0
4 3 0
3 0

## Slide 36: Example: GOOD GADGET
1
2
4
3
0
2 1 0
2 0
1 3 0
1 0
4 3 0
4 2 0
3 0

## Slide 37: Example: GOOD GADGET (Solution)
1
2
4
3
0
2 1 0
2 0
1 3 0
1 0
4 3 0
4 2 0
3 0

## Slide 38: A Stable Paths Problem may have multiple solutions
First solution
1
0
2
1 2 0
1 0
1
0
2
1
0
2
2 1 0
2 0
1 2 0
1 0
2 1 0
2 0
1 2 0
1 0
2 1 0
2 0
Second solution
DISAGREE

## Slide 39: Example: NAUGHTY GADGET
1
2
4
3
0
2 1 0
2 0
1 3 0
1 0
4 3 0
4 2 0
3 4 2 0
3 0

## Slide 40: Example: NAUGHTY GADGET (Solution 1)
1
2
4
3
0
2 1 0
2 0
1 3 0
1 0
4 3 0
4 2 0
3 4 2 0
3 0

## Slide 41: Example: NAUGHTY GADGET (Solution 2)
1
2
4
3
0
2 1 0
2 0
1 3 0
1 0
4 3 0
4 2 0
3 4 2 0
3 0

## Slide 42: SPP helps explain possibility of BGP divergence
BGP is not guaranteed to converge to a stable routing. Policy inconsistencies can lead to “livelock” protocol oscillations.
See “Persistent Route Oscillations in Inter-domain Routing” by K. Varadhan, R. Govindan, and D. Estrin. ISI report, 1996
Solvable
Can Diverge
must converge
must diverge
The SPP view :
Notes: If you can’t solve this problem, then you don’t understand the protocol

## Slide 43: Example: NAUGHTY GADGET
1
2
4
3
0
2 1 0
2 0
1 3 0
1 0
4 3 0
4 2 0
3 4 2 0
3 0

## Slide 44: Example: BAD GADGET
1
2
4
3
0
2 1 0
2 0
1 3 0
1 0
4 2 0
4 3 0
3 4 2 0
3 0

## Slide 45: Example: BAD GADGET
1
2
4
3
0
2 1 0
2 0
1 3 0
1 0
4 2 0
4 3 0
3 4 2 0
3 0
2 chooses (2 0)
4 chooses (4 2 0)
3 chooses (3 4 2 0)
1 chooses (1 0)

## Slide 46: Example: BAD GADGET
1
2
4
3
0
2 1 0
2 0
1 3 0
1 0
4 2 0
4 3 0
3 4 2 0
3 0
… 2 chooses (2 1 0) …

## Slide 47: Example: BAD GADGET
1
2
4
3
0
2 1 0
2 0
1 3 0
1 0
4 2 0
4 3 0
3 4 2 0
3 0
… 3 chooses (3 0) …

## Slide 48: Example: BAD GADGET
1
2
4
3
0
2 1 0
2 0
1 3 0
1 0
4 2 0
4 3 0
3 4 2 0
3 0
… 1 chooses (1 3 0) …

## Slide 49: Example: BAD GADGET
1
2
4
3
0
2 1 0
2 0
1 3 0
1 0
4 2 0
4 3 0
3 4 2 0
3 0
… 2 chooses (2 0) …

## Slide 50: Example: BAD GADGET
1
2
4
3
0
2 1 0
2 0
1 3 0
1 0
4 2 0
4 3 0
3 4 2 0
3 0
… 3 chooses (3 4 2 0) …
LOOP !

## Slide 51: BAD GADGET : No Solution
2
0
3
1
2 1 0
2 0
1 3 0
1 0
3 4 2 0
3 0
4
4 2 0
4 3 0
With a BGP-like
protocol, each node
will do the best it
can, so at least one
node will always have
the opportunity to
improve its path.
Result :
persistent oscillation.

## Slide 52: SURPRISE : Beware of Backup Policies
2
0
3
1
2 1 0
2 0
1 3 0
1 0
3 4 2 0
3 0
4
4 0
4 2 0
4 3 0
Becomes BAD GADGET if link
(4, 0) goes down.
BGP is not robust :
it is not guaranteed
to recover from
network failures.

## Slide 53: PRECARIOUS
1
0
2
1 2 0
1 0
2 1 0
2 0
3
4
5
6
5 3 1 0
5 6 3 1 2 0
5 3 1 2 0
6 3 1 0
6 4 3 1 2 0
6 3 1 2 0
4 3 1 0
4 5 3 1 2 0
4 3 1 2 0
3 1 0
3 1 2 0
As with DISAGREE, this part
has two distinct solutions
This part has a solution only
when node 1 is assigned the
direct path (1 0).
Has a solution, but can get “trapped”

## Slide 54: Theoretical Results
The problem of determining whether an instance of stable paths problem is solvable is NP-complete
Shortest path route selection is provably safe

## Slide 55: Convergence in the real-world?
[Labovitz99] Experimental results from two year study which measured 150,000 BGP faults injected into peering sessions at several IXPs
Found
  Internet averages 3 minutes to converge after failover
  Some multihomed failovers (short to long ASPath) require 15 minutes

## Slide 56: BGP Convergence Example
R
AS0
AS1
AS2
AS3
*B R via AS3
B R via AS0,AS3
B R via AS2,AS3
*B R via AS3
B R via AS0,AS3
B R via AS1,AS3
*B R via AS3
B R via AS1,AS3
B R via AS2,AS3
AS0
AS1
AS2
*
*
*
*B R via 203
*B R via 013
B R via 103

## Slide 57: Convergence Result
If we assume
    unbounded delay on BGP processing and propagation
    Full BGP mesh BGP peers
    Constrained shortest path first selection algorithm
BGP is O(N!), where N number of default-free BGP speakers
  There exists possible ordering of messages such that BGP will explore all possible ASPaths of all possible lengths

## Slide 58: An SPP May Have No Solution
2
0
3
1
2 1 0
2 0
1 3 0
1 0
3 2 0
3 0
4
3
58

## Slide 59: Avoiding BGP Instability
Detecting conflicting policies
  Computationally expensive
  Requires too much cooperation
Detecting oscillations
  Observing the repetitive BGP routing messages
Restricted routing policies and topologies
  Policies based on business relationships
59

## Slide 60: AS (Autonomous System) Business Relationships
60

## Slide 61: Customer-Provider Relationship
Customer pays provider for access to Internet
  Provider exports its customer routes to everybody
  Customer exports provider routes only to its customers
d
d
provider
customer
customer
provider
Traffic to customer
Traffic from customer
advertisements
traffic
61

## Slide 62: Peer-Peer Relationship
Peers exchange traffic between their customers
  AS exports only customer routes to a peer
  AS exports a peer’s routes only to its customers
peer
peer
Traffic to/from the peer and its customers
d
advertisements
traffic
62

## Slide 63: Hierarchical AS Relationships
Provider-customer graph is directed and acyclic
  If u is a customer of v and v is a customer of w
  … then w is not a customer of u
u
v
w
63

## Slide 64: Valid and Invalid Paths
2
3
1
d
4
5
6
7
8
Provider-Customer
Peer-Peer
Path 1 2 d
Path 7 d
Path 5 8 d
Path 6 4 3 d
Path 8 5 d
Path 6 5 d
Path 1 4 3 d
64
A) Valid B) Invalid

## Slide 65: Valid and Invalid Paths
2
3
1
d
4
5
6
7
8
Provider-Customer
Peer-Peer
Valid paths: “1 2 d” and “7 d”
Invalid path: “5 8 d”
65

## Slide 66: Valid and Invalid Paths
2
3
1
d
4
5
6
7
8
Provider-Customer
Peer-Peer
Valid paths: “6 4 3 d” and “8 5 d”
Invalid paths: “6 5 d” and “1 4 3 d”
66

## Slide 67: Local Control, Global Stability: “Gao-Rexford Conditions”
Route export
  Don’t export routes learned from a peer or provider to another peer or provider
Global topology
  Provider-customer relationship graph is acyclic
  E.g., my customer’s customer is not my provider
Route selection
  Prefer routes through customers over routes through peers and providers
Guaranteed to converge to unique, stable solution
67

## Slide 68: Conclusions
The only constant is change
  Planned topology and configuration changes
  Unplanned failure and recovery
Routing-protocol convergence
  Transient period of disagreement
  Blackholes, loops, and out-of-order packets
Routing instability
  Permanent conflicts in routing policy
  Leading to bi-stability or oscillation
68