## Slide 1: Transport Layer
Dr. Yingwu Zhu
Chapter 3.1, 3.2, 3,3 and 3.5

## Slide 2: Transport Layer: Where Are We?

## Slide 3: IP Protocol Stack: Key Abstractions
Transport layer is where we “pay the piper”
  Provide applications with good abstractions
  Without support or feedback from the network
Best-effort local packet delivery
Best-effort global packet delivery
Reliable streams
Applications
Messages
Link
Network
Transport
Application

## Slide 4: Transport-Layer Protocols
reliable, in-order delivery (TCP)
  congestion control
  flow control
  connection setup
unreliable, unordered delivery: UDP
services not available:
  delay guarantees
  bandwidth guarantees
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
logical end-end transport

## Slide 5: Transport Protocols
Logical communication between processes
  Sender divides a message into segments
  Receiver reassembles segments into message
Transport services
  (De)multiplexing packets
  Detecting corrupted data
  Optionally: reliable delivery, flow control, congestion control…

## Slide 6: Two Basic Transport Features
Demultiplexing: port numbers
Error detection: checksums
Web server
(port 80)
Client host
Server host 128.2.194.242
Echo server
(port 7)
Service request for
128.2.194.242:80
(i.e., the Web server)
OS
Client
IP
payload
detect corruption
6

## Slide 7: UDP

## Slide 8: UDP: User Datagram Protocol [RFC 768]
“no frills,” “bare bones” Internet transport protocol
“best effort” service, UDP segments may be:
  lost
  delivered out of order to app
connectionless:
  no handshaking between UDP sender, receiver
  each UDP segment handled independently of others
Why is there a UDP?
no connection establishment (which can add delay)
simple: no connection state at sender, receiver
small segment header: 8 bytes
  TCP header: 20 bytes
no congestion control: UDP can blast away as fast as desired

## Slide 9: UDP: more
Often used for streaming multimedia apps
  loss tolerant
  rate sensitive
Other UDP uses
  DNS
  SNMP
Reliable transfer over UDP: add reliability at application layer
  application-specific error recovery!
source port #
dest port #
32 bits
Application
data
(message)
UDP segment format
length
checksum
Length, in
bytes of UDP
segment,
including
header

## Slide 10: UDP checksum
Sender:
treat segment contents as sequence of 16-bit integers
checksum: addition (1’s complement sum) of segment contents
sender puts checksum value into UDP checksum field
Receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  NO - error detected
  YES - no error detected. But maybe errors nonetheless? ….
Goal: detect “errors” (e.g., flipped bits) in transmitted segment

## Slide 11: Internet Checksum Example
Note
  When adding numbers, a carryout from the most significant bit needs to be added to the result
Example: add two 16-bit integers
1 1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
1 0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
wraparound
sum
checksum
Notes: Kurose and Ross forgot to say anything about wrapping the carry and adding it to low order bit

## Slide 12: Advantages of UDP
Fine-grain control
  UDP sends as soon as the application writes
No connection set-up delay
  UDP sends without establishing a connection
No connection state
  No buffers, parameters, sequence #s, etc.
Small header overhead
  UDP header is only eight-bytes long

## Slide 13: TCP

## Slide 14: Transmission Control Protocol (TCP)
Stream-of-bytes service
  Sends and receives a stream of bytes
Reliable, in-order delivery
  Corruption: checksums
  Detect loss/reordering: sequence numbers
  Reliable delivery: acknowledgments and retransmissions
Connection oriented
  Explicit set-up and tear-down of TCP connection
Flow control
  Prevent overflow of the receiver’s buffer space
Congestion control
  Adapt to network congestion for the greater good

## Slide 15: TCP Offers Byte Stream Service: Breaking a Stream of Bytes into TCP Segments

## Slide 16: TCP “Stream of Bytes” Service
Byte 0
Byte 1
Byte 2
Byte 3
Byte 0
Byte 1
Byte 2
Byte 3
Host A
Host B
Byte 80
Byte 80
16

## Slide 17: …Emulated Using TCP “Segments”
Byte 0
Byte 1
Byte 2
Byte 3
Byte 0
Byte 1
Byte 2
Byte 3
Host A
Host B
Byte 80
TCP Data
TCP Data
Byte 80
Segment sent when:
Segment full (Max Segment Size),
Not full, but times out, or
“Pushed” by application
17

## Slide 18: TCP Segment
IP packet
  No bigger than Maximum Transmission Unit (MTU)
  E.g., up to 1500 bytes on an Ethernet link
TCP packet
  IP packet with a TCP header and data inside
  TCP header is typically 20 bytes long
TCP segment
  No more than Maximum Segment Size (MSS) bytes
  E.g., up to 1460 consecutive bytes from the stream
IP Hdr
IP Data
TCP Hdr
TCP Data (segment)
18

## Slide 19: TCP segment structure
source port #
dest port #
32 bits
application
data
(variable length)
sequence number
acknowledgement number
Receive window
Urg data pnter
checksum
F
S
R
P
A
U
head
len
not
used
Options (variable length)
URG: urgent data
(generally not used)
ACK: ACK #
valid
PSH: push data now
(generally not used)
RST, SYN, FIN:
connection estab
(setup, teardown
commands)
# bytes
rcvr willing
to accept
counting
by bytes
of data
(not segments!)
Internet
checksum
(as in UDP)
The head length is in terms of 32-bit words

## Slide 20: TCP: Sequence Numbers

## Slide 21: Sequence Number
Host A
Host B
TCP Data
TCP Data
ISN (initial sequence number)
Sequence number = 1st byte
Byte 81
21

## Slide 22: Initial Sequence Number (ISN)
Sequence number for the very first byte
  E.g., Why not a de facto ISN of 0?
Practical issue: reuse of port numbers
  Port numbers must (eventually) get used again
  … and an old packet may still be in flight
  … and associated with the new connection
So, TCP must change the ISN over time
  Set from a 32-bit clock that ticks every 4 microsec
  … which wraps around once every 4.55 hours!
22

## Slide 23: Reliable Delivery on a Lossy Channel With Bit Errors

## Slide 24: Challenges of Reliable Data Transfer
Over a perfectly reliable channel: Done
Over a channel with bit errors
  Receiver detects errors and requests retransmission
Over a lossy channel with bit errors
  Some data missing, others corrupted
  Receiver cannot easily detect loss
Over a channel that may reorder packets
  Receiver cannot easily distinguish loss vs. out-of-order
24

## Slide 25: An Analogy
Alice and Bob are talking
  What if Alice couldn’t understand Bob?
  Bob asks Alice to repeat what she said
What if Bob hasn’t heard Alice for a while?
  Is Alice just being quiet? Has she lost reception?
  How long should Bob just keep on talking?
  Maybe Alice should periodically say “uh huh”
  … or Bob should ask “Can you hear me now?”
25

## Slide 26: Take-Aways from the Example
Acknowledgments from receiver
  Positive: “okay” or “uh huh” or “ACK”
  Negative: “please repeat that” or “NACK”
Retransmission by the sender
  After not receiving an “ACK”
  After receiving a “NACK”
Timeout by the sender (“stop and wait”)
  Don’t wait forever without some acknowledgment
26

## Slide 27: TCP Support for Reliable Delivery
Detect bit errors: checksum
  Used to detect corrupted data at the receiver
  …leading the receiver to drop the packet
Detect missing data: sequence number
  Used to detect a gap in the stream of bytes
  ... and for putting the data back in order
Recover from lost data: retransmission
  Sender retransmits lost or corrupted data
  Two main ways to detect lost packets
27

## Slide 28: TCP Acknowledgments
Host A
Host B
TCP Data
TCP Data
ISN (initial sequence number)
Sequence number = 1st byte
ACK sequence number = next expected byte
28

## Slide 29: Automatic Repeat reQuest (ARQ)
ACK and timeouts
  Receiver sends ACK when it receives packet
  Sender waits for ACK and times out
Simplest ARQ protocol
  Stop and wait
  Send a packet, stop and wait until ACK arrives
Time
Packet
ACK
Timeout
Sender
Receiver

## Slide 30: Quick TCP Math
Initial Seq No = 501. Sender sends 4500 bytes successfully acknowledged. Next sequence number to send is:
  (A) 5000 (B) 5001 (C) 5002
Next 1000 byte TCP segment received. Receiver acknowledges with ACK number:
  (A) 5001 (B) 6000 (C) 6001

## Slide 31: Quick TCP Math
Initial Seq No = 501. Sender sends 4500 bytes successfully acknowledged. Next sequence number to send is:
  (A) 5000 (B) 5001 (C) 5002
Next 1000 byte TCP segment received. Receiver acknowledges with ACK number:
  (A) 5001 (B) 6000 (C) 6001

## Slide 32: Flow Control: TCP Sliding Window

## Slide 33: Motivation for Sliding Window
Stop-and-wait is inefficient (from RDT protocol discussions)
  Only one TCP segment is “in flight” at a time
Consider: 1.5 Mbps link with 50 ms round-trip-time (RTT)
  Assume TCP segment size of 1 KB (8 Kbits)
  8 Kbits/segment at 50 msec/segment  160 Kbps
  That’s 11% of the capacity of 1.5 Mbps link
33

## Slide 34: Sliding Window
Allow a larger amount of data “in flight”
  Allow sender to get ahead of the receiver
  … though not too far ahead
Sending process
Receiving process
Last byte ACKed
Last byte sent
TCP
TCP
Next byte expected
Last byte written
Last byte read
Last byte received
34

## Slide 35: Sliding Window
Last byte ACKed
Last byte sent
TCP
TCP
Next byte expected
Last byte received
35
Receive window size
  Amount that can be sent without acknowledgment
  Receiver must be able to store this amount of data
Receiver tells the sender the window
  Tells the sender the amount of free space left
Window Size
OK to send
}

## Slide 36: TCP Flow Control
receive side of TCP connection has a receive buffer:
speed-matching service: matching the send rate to the receiving app’s drain rate
app process may be slow at reading from buffer
sender won’t overflow
receiver’s buffer by
transmitting too much,
too fast
flow control

## Slide 37: TCP Flow control: how it works
(Suppose TCP receiver discards out-of-order segments)
spare room in buffer
= RcvWindow
= RcvBuffer-[LastByteRcvd - LastByteRead]
Rcvr advertises spare room by including value of RcvWindow in segments
Sender limits unACKed data to RcvWindow
  guarantees receive buffer doesn’t overflow

## Slide 38: TCP Flow control: how it works
If the sender gets notified of RcvWindow = 0 from the receiver?
  Problem: the sender never able to send data to the receiver
  Why: the receiver will not send segments to the sender unless having data/ack to send
  Solution: the sender continues to send a segment with 1 data byte when RcvWindow = 0; then the receiver will update it.

## Slide 39: Optimizing Retransmissions

## Slide 40: Reasons for Retransmission
Packet
ACK
Timeout
Packet
ACK
Timeout
Packet
Timeout
Packet
ACK
Timeout
Packet
ACK
Timeout
Packet
ACK
Timeout
ACK lost
DUPLICATE PACKET
Packet lost
Early timeout
DUPLICATE PACKETS
Notes: Application may get duplicates in the case of early timeouts

## Slide 41: How Long Should Sender Wait?
Sender sets a timeout to wait for an ACK
  Too short: wasted retransmissions
  Too long: excessive delays when packet lost
TCP sets timeout as a function of the RTT
  Expect ACK to arrive after an “round-trip time”
  … plus a fudge factor to account for queuing
But, how does the sender know the RTT?
  Running average of delay to receive an ACK
41

## Slide 42: Example RTT Estimation
42

## Slide 43: Still, timeouts are slow (≈RTT)
When packet n is lost…
  … packets n+1, n+2, and so on may get through
Exploit the ACKs of these packets
  ACK says receiver is still awaiting nth packet
  Duplicate ACKs suggest later packets arrived
  Sender uses “duplicate ACKs” as a hint
Fast retransmission
  Retransmit after “triple duplicate ACK”
43

## Slide 44: Effectiveness of Fast Retransmit
When does Fast Retransmit work best?
  High likelihood of many packets in flight
  Long data transfers, large window size, …
Implications for Web traffic
  Most Web transfers are short (e.g., 10 packets)
    So, often there aren’t many packets in flight
  Making fast retransmit is less likely to “kick in”
    Forcing users to click “reload” more often…
44

## Slide 45: Effectiveness of Fast Retransmit
When does Fast Retransmit work best?
  (A) Short data transfers
  (B) Large window size
  (C) Small RTT networks
45

## Slide 46: Starting and Ending a Connection: TCP Handshakes

## Slide 47: Establishing a TCP Connection
Three-way handshake to establish connection
  Host A sends a SYN (open) to the host B
  Host B returns a SYN acknowledgment (SYN ACK)
  Host A sends an ACK to acknowledge the SYN ACK
SYN
SYN ACK
ACK
Data
A
B
Data
Each host tells its ISN to the other host.

## Slide 48: TCP Header
Source port
Destination port
Sequence number
Acknowledgment
Advertised window
HdrLen
Flags
0
Checksum
Urgent pointer
Options (variable)
Data
Flags:
SYN
FIN
RST
PSH
URG
ACK

## Slide 49: Step 1: A’s Initial SYN Packet
A’s port
B’s port
A’s Initial Sequence Number
Acknowledgment
Advertised window
20
Flags
0
Checksum
Urgent pointer
Options (variable)
Flags:
SYN
FIN
RST
PSH
URG
ACK
A tells B it wants to open a connection…

## Slide 50: Step 2: B’s SYN-ACK Packet
B’s port
A’s port
B’s Initial Sequence Number
A’s ISN plus 1
Advertised window
20
Flags
0
Checksum
Urgent pointer
Options (variable)
Flags:
SYN
FIN
RST
PSH
URG
ACK
B tells A it accepts, and is ready to hear the next byte…
… upon receiving this packet, A can start sending data
50

## Slide 51: Step 3: A’s ACK of the SYN-ACK
A’s port
B’s port
B’s ISN plus 1
Advertised window
20
Flags
0
Checksum
Urgent pointer
Options (variable)
Flags:
SYN
FIN
RST
PSH
URG
ACK
A tells B it is okay to start sending
Sequence number
… upon receiving this packet, B can start sending data
51

## Slide 52: SYN Loss and Web Downloads
Upon sending SYN, sender sets a timer
  If SYN lost, timer expires before SYN-ACK received
  Sender retransmits SYN
How should the TCP sender set the timer?
  No idea how far away the receiver is
  Some TCPs use default of 3 or 6 seconds
Implications for web download
  User gets impatient and hits reload
  … Users aborts connection, initiates new socket
  Essentially, forces a fast send of a new SYN!
52

## Slide 53: SYN flood attack
“A SYN flood is a form of denial-of-service attack in which an attacker sends a succession of SYN requests to a target's system in an attempt to consume enough server resources to make the system unresponsive to legitimate traffic”, from Wikipedia
Half-open TCP connections consume resources at the server

## Slide 54: Tearing Down the Connection
Closing (each end of) the connection
  Finish (FIN) to close and receive remaining bytes
  And other host sends a FIN ACK to acknowledge
  Reset (RST) to close and not receive remaining bytes
SYN
SYN ACK
ACK
Data
FIN
ACK
ACK
time
A
B
FIN
ACK
54

## Slide 55: Sending/Receiving the FIN Packet
Sending a FIN: close()
  Process is done sending data via socket
  Process invokes “close()”
  Once TCP has sent all the outstanding bytes…
  … then TCP sends a FIN
Receiving a FIN: EOF
  Process is reading data from socket
  Eventually, read call returns an EOF
55

## Slide 56: TCP Connection Management: Connection Tear-down
Closing a connection:
Two double handshakes
client closes socket: clientSocket.close();
Step 1: client end system sends TCP FIN control segment to server
Step 2: server receives FIN, replies with ACK, sends FIN.
client
FIN
server
ACK
ACK
FIN
close
close
closed
timed wait

## Slide 57: TCP Connection Management (cont.)
Step 3: client receives FIN, replies with ACK.
  Enters “timed wait” - will respond with ACK to received FINs
Step 4: server, receives ACK. Connection closed.
Note: with small modification, can handle simultaneous FINs.
client
FIN
server
ACK
ACK
FIN
closing
closing
closed
timed wait
closed

## Slide 58: TCP Connection Management (cont)
TCP client
lifecycle
TCP server
lifecycle

## Slide 59: Conclusions
Transport protocols
  Multiplexing and demultiplexing
  Checksum-based error detection
  Sequence numbers
  TCP Retransmission
  TCP Window-based flow control
59